This manual is intended to be used as an introductory safety guide only.  Instructor should add additional training as needed.

| STUDY GUIDE EXTENSION lADDER SAFETY | Page 1 Name:______________________________ Class Or Period______________________ Date Of Instruction: ____________________ |
| --- | --- |
| _______ | 1. | Proper PPE must be used. Safety glasses and substantial footwear are required. |
| _______ | 2. | Study the operation, maintenance, or safety manuals for the machine, equipment, and tools to be used. |
| _______ | 3. | Never operate machines, equipment, or tools without instructor’s permission. |
| _______ | 4. | Secure/remove all loose clothing. |
| _______ | 5. | Remove all jewelry. |
| _______ | 6. | Always inspect the rung locks before using ladder. |
| _______ | 7. | Always reposition a ladder from the bottom, not the top. |
| _______ | 8. | Check to make sure the section locking mechanism is fully hooked over the desired rung. |
| _______ | 9. | Also check that all ropes used for raising and lowering the extension are untangled and free to move. |
| _______ | 10. | Never pull an extension ladder farther apart then is safe. For ladders up to 36 feet long there must be an overlap of at least 3 feet. Ladders up to 48 feet require at least 4 feet of overlap, and ladders up to 60 feet require at least 5 feet of overlap. |
| _______ | 11. | Never stand higher than the safe standing level on the ladder. This is the fourth rung from the top. |
| _______ | 12. | Haul materials up on a line rather than carrying them up an extension ladder. |
| _______ | 13. | Always climb/descend facing the ladder, centered between the rails and with a firm grasp on the rungs. |
| _______ | 14. | Never move more than one step at a time, keeping each foot firmly in place. |
| _______ | 15. | A ladder should be used at an angle where the horizontal distance from the top support to the foot of the ladder is ¼ the working length of the ladder (length along ladder between the foot and top support). |
| _______ | 16. | It is recommended that whenever possible a competent helper hold the bottom of the ladder while it is being used. |

| TEST EXTENSION LADDER SAFETY | Page 1 Name:__________________________________ Class Or Period:__________________________ Date:________________ Score:_____________ |
| --- | --- |
| _______1. | Proper PPE must be used. _____ and substantial footwear are required. | Select the correct word that completes each sentence. Then write the corresponding letter on the line preceding the sentence. |
| _______2. | Study the operation, maintenance, and safety _____ for the machine, equipment, and tools to be used. |  |
| _______3. | Never operate machines, equipment, or tools without instructor’s ____. |  |
| _______4. | Secure/remove all loose ____. |  |
| _______5. | _____ all jewelry. |  |
| _______6. | Always inspect the ____ before using ladder. |  |
| _______7. | Always reposition a ladder from the _____. |  |
| _______8. | Check to make sure the section _____ is fully hooked over the desired rung. |  |
| _______9. | Also check that all ____ used for raising and lowering the extension are untangled. |  |
| _______10. | For ladders up to 36 feet long there must be an overlap of at least _____ feet. |  |
| _______11. | Never stand higher than the _____ rung from the top. |  |
| _______12. | Haul materials up on a ____. |  |
| _______13. | Always climb/descend facing the ladder, with a _____ on the rungs. |  |
| _______14. | Never move more than one _____ at a time. |  |
| _______15. | A ladder should be used at an angle where the horizontal distance from the top support to the foot of the ladder is ____ the working length of the ladder (length along ladder between the foot and top support). |  |
| _______16. | It is recommended that whenever possible a _____ hold the bottom of the ladder while it is being used. |  |

| ANSWER KEY EXTENSION LADDER SAFETY |  |
| --- | --- |
| Statement Number | Correct Letter and Words | Statement Number | Correct Letter and Words |
| 1 | C safety glasses | 9 | I ropes |
| 2 | H manuals | 10 | F three |
| 3 | E permission | 11 | B fourth |
| 4 | P clothing | 12 | K line |
| 5 | O remove | 13 | G firm grasp |
| 6 | J rung locks | 14 | D rung |
| 7 | A bottom | 15 | N 1/4 |
| 8 | L locking mechanism | 16 | M competent helper |

# Text boxes

Typical Extension Ladder

A.	bottom

B.	fourth

C.	safety glasses

D.	rung

E.	permission

F.	three

G.	firm grasp

H.	manuals

I.	ropes

J.	rung locks

K.	line

L.	locking mechanism

M.	competent helper

N.	¼

O.	remove

P.	clothing

Applicable to OSHA 10-Hour Card

Subpart I: PPE,  Subpart D: Walking and Working Surfaces, Subpart Z:  Hazard Communication, Subpart Z: Introduction to Industrial Hygiene, Bloodborne Pathogen, and/or Ergonomics